## Slide 1
AVs
TINYML · EDGE AI CAPSTONE PROJECT
AVsentry
AI-Based Smart Room Safety & Environmental Monitoring System
Multi-sensor Edge AI reasoning — intrusion detection and environmental discomfort, running entirely on-device.
Victor G. Ahmedu 400L Electrical & Electronics Engineering · FUTMINNA LET INNOVATION IT CAPSTONE PROJECT
1 / 10

## Slide 2
01 · THE PROBLEM
Rooms lack low-cost, intelligent monitoring
!
Security gap
Simple rooms often have no monitoring at all, or single-purpose alarms that only detect motion with zero context.
~
Environmental risk
Heat and humidity extremes go unnoticed until they cause discomfort or damage.
=
Rule-based limits
Traditional systems use rigid per-sensor thresholds — they cannot reason about combinations.
C
Cloud dependency
Most “smart” solutions require constant internet and cloud processing for a simple room.
2 / 10

## Slide 3
02 · OBJECTIVES
What this project set out to solve
1
Detect intrusion / unexpected presence using a passive-IR sensor.
2
Detect environmental discomfort — excess heat or humidity — using a DHT11 sensor.
3
Reason over combined conditions (e.g. occupied + overheating), not isolated thresholds.
4
Run the entire decision-making process on-device — no cloud or constant connectivity.
5
Respond physically and instantly via buzzer, status LEDs, and a servo-driven alert.
3 / 10

## Slide 4
03 · SYSTEM ARCHITECTURE
Sensors → Edge AI → Actuators
DHT11
Temp / Humidity
→
IR Sensor
Presence
→
NodeMCU ESP8266
On-device ML inference
→
Buzzer
→
LEDs
→
Servo
Key architectural point
Training happens once, offline, on a laptop. Inference — the actual decision-making — happens continuously, entirely on the NodeMCU. No WiFi, cloud, or host machine is needed at runtime. This is what qualifies the system as genuine Edge AI / TinyML.
4 / 10

## Slide 5
04 · HARDWARE
Bill of components
Component | Role
NodeMCU ESP8266 | Microcontroller — runs sensor reads and on-device ML inference
DHT11 | Temperature & humidity sensing
IR obstacle sensor | Presence / motion detection (digital HIGH/LOW)
Passive buzzer | Audible alert on intrusion
Status LEDs (green / red) | At-a-glance system state indicator
Servo motor | Physical alert action on confirmed intrusion
5 / 10

## Slide 6
05 · WHY TINYML
Why a decision tree, not a neural network
X
TensorFlow Lite Micro
ESP8266 has roughly 50KB of usable RAM and no FPU. A full TFLite Micro runtime is impractical to fit and run reliably at this scale.
✓
Decision Tree → C code
A scikit-learn Decision Tree, trained offline, is compiled directly into plain C if-else logic using micromlgen. No ML runtime library is needed on-device.
Result
A genuinely learned, multi-feature decision boundary — not hardcoded thresholds — running in microseconds on a $5 microcontroller.
6 / 10

## Slide 7
06 · DATA & LABELING
Five classes, physically simulated and labeled
Normal
Ambient room conditions, no presence.
Discomfort — Hot
Temperature above threshold.
Discomfort — Humid
Humidity above threshold.
Occupied + Uncomfortable
Presence combined with poor conditions.
Intrusion
Presence detected under otherwise normal conditions.
Method
A custom Python tool logged live serial sensor data straight into a labeled CSV during physically staged sessions (over 950 rows of labeled readings), tagging every row with the active scenario in real time.
7 / 10

## Slide 8
07 · MODEL PERFORMANCE
Training results
93%
Overall test accuracy
3
Input features — temp, humidity, IR
100%
Precision & recall — Normal and Intrusion classes
Where confusion remains
Residual misclassification sits only between the two heat-related classes (Discomfort-Hot ↔ Occupied-Uncomfortable) — both genuinely share overlapping temperature ranges. Critically, intrusion detection is unaffected.
8 / 10

## Slide 9
08 · ENGINEERING JOURNEY
Two real bugs, diagnosed and fixed
T
The “hour” feature trap
An early version used time-of-day (via WiFi + NTP) to separate intrusion from daytime presence. It backfired: the model only ever saw a few training hours, so real-world hours it had never seen caused false intrusion alarms.
Fix: removed the time feature entirely, simplifying the system and removing the WiFi dependency — improving robustness at any hour.
D
Label contamination
During data collection, presence was toggled on and off within single labeled sessions, leaving some “intrusion” rows with the sensor actually reading clear.
Fix: programmatically filtered out every row where the label and the live IR state disagreed, then retrained — resolving false positives.
9 / 10

## Slide 10
AVs
AVsentry
A working, on-device Edge AI safety system
✓
Fully functional multi-sensor system reasoning over combined conditions — not simple thresholds.
✓
Trained model runs entirely on a $5 microcontroller, with zero runtime cloud or network dependency.
✓
Physically verified across all five classes with correct buzzer, LED, and servo responses.
✓
Future work: lightweight RTC time-context, gas/smoke sensing, a proper enclosure, and mobile alerts.
Thank you!
Victor · FUTMINNA & LET INNOVATIONS · Electrical & Electronics Engineering
10 / 10